## Slide 1
FUTURDATA THESIS
Disassembly Guide
Bialetti Gioia
PPTX export • 7 action group(s) • depth: DepthMode.FULL • schema 1.1
Nominal weight 2500 g
PRODUCT IMAGE
Bialetti Gioia
1 / 13

## Slide 2
PROJECT OVERVIEW
Export scope and model summary
PRODUCT ID
2046965323920
ACTION GROUPS
7
BOM COMPONENTS
18
VALIDATION ISSUES
0
PRODUCT DATA
Name: Bialetti Gioia Weight: 2500 g Material: Unknown Color: Unknown Depth mode: DepthMode.FULL
EXPORT BEHAVIOUR
• Parent operation and atomic actions stay grouped. • Output components and remaining assembly are shown. • Text and images remain editable in PowerPoint. • Unknown branch sources are never guessed. • Source JSON is opened read-only and never modified.
Bialetti Gioia
2 / 13

## Slide 3
PREPARATION
Tools and safety notices
Aggregated from step-level and atomic-action metadata.
TOOLS REQUIRED
• Soft cloth • Torx T10 screwdriver • Phillips PH1 screwdriver • Plastic pry tool • Hands • JST connector tool • Phillips PH0 screwdriver • Container • Hose clamp pliers • Side cutters • Heat-resistant gloves (precaution) • 10 mm wrench • Bench vice with soft jaws • Hex key (typically 4 mm) • Soft mallet • Press / saw (destructive option)
SAFETY NOTICES
• No safety notices are specified in this model.
Bialetti Gioia
3 / 13

## Slide 4
BILL OF MATERIALS
Recovered components — page 1 of 2
ID | Component | Weight | Material | Color | Quality | Destination
2046970 843664 | Outer shell | 260 g | Unknown | Unknown | — | —
2046984 185360 | Water tank | 150 g | Unknown | Unknown | — | —
2046967 305744 | Capsule drawer | 60 g | Unknown | Unknown | — | —
2046984 187728 | Capsule lever | 130 g | Unknown | Unknown | — | —
2046984 186576 | Button panel | 35 g | Unknown | Unknown | — | —
2046970 954192 | Capsule sensor | 18 g | Unknown | Unknown | — | —
2046878 817808 | Vibration pump | 185 g | Unknown | Unknown | — | —
2047098 762832 | Silicone tubing | 22 g | Unknown | Unknown | — | —
2046970 849104 | Flow meter | 28 g | Unknown | Unknown | — | —
Bialetti Gioia
4 / 13

## Slide 5
BILL OF MATERIALS
Recovered components — page 2 of 2
ID | Component | Weight | Material | Color | Quality | Destination
2047098 764560 | Main PCB | 55 g | Unknown | Unknown | — | —
2047097 655888 | Wiring harness | 70 g | Unknown | Unknown | — | —
2046879 036304 | Power cord | 140 g | Unknown | Unknown | — | —
2046885 877712 | Chassis frame | 967 g | Unknown | Unknown | — | —
2046881 532816 | Thermoblock fasteners | 20 g | Unknown | Unknown | — | —
2046878 694160 | Heating element | 45 g | Unknown | Unknown | — | —
2046994 986000 | Safety thermostat | 15 g | Unknown | Unknown | — | —
2046965 449232 | Aluminium body | 240 g | Unknown | Unknown | — | —
2046884 534032 | Stainless tube | 60 g | Unknown | Unknown | — | —
Bialetti Gioia
5 / 13

## Slide 6
ACTION GROUP 1
Open outer shell from chassis
Atomic actions are grouped under their parent disassembly operation.
Source: Bialetti Gioia (2500 g)
explicit source
ATOMIC ACTIONS
1
Place the machine upside-down on a soft cloth so the bottom plate is accessible; remove any residual water from the tank seat to avoid leaks.
2
Unscrew the 4 Torx T10 screws located at the corners of the bottom plate.
3
Unscrew the 2 Phillips PH1 screws behind the rear panel, near the power-cord grommet.
4
Release the 4 internal plastic clips along the vertical edges by gently prying with a flat plastic tool.
5
Lift the upper shell vertically, keeping it parallel to the base, to separate it from the internal chassis.
RESULT
• Outer shell (260 g)
CONTINUES AS
• Chassis (full) (2240 g)
TOOLS
Soft cloth, Torx T10 screwdriver, Phillips PH1 screwdriver, Plastic pry tool, Hands
Bialetti Gioia
6 / 13

## Slide 7
ACTION GROUP 2
Remove user-accessible parts (tank, drawer, lever)
Atomic actions are grouped under their parent disassembly operation.
Source: Chassis (full) (2240 g)
explicit source
ATOMIC ACTIONS
1
Lift out the 0.5 L removable water tank from its seat at the rear of the machine.
2
Pull out the used-capsule drawer from the front-bottom slot.
3
Release the 2 Phillips PH1 screws of the capsule lever / brewing-group assembly and lift it out.
RESULT
• Water tank (150 g) • Capsule drawer (60 g) • Capsule lever (130 g)
CONTINUES AS
• Chassis (no user parts) (1900 g)
TOOLS
Hands, Phillips PH1 screwdriver
Bialetti Gioia
7 / 13

## Slide 8
ACTION GROUP 3
Disconnect and remove the front control-panel assembly
Atomic actions are grouped under their parent disassembly operation.
Source: Chassis (no user parts) (1900 g)
explicit source
ATOMIC ACTIONS
1
Unplug the JST-XH 4-pin connector that links the front button board to the main PCB; press the latch before pulling.
2
Unplug the JST-PH 2-pin connector of the aluminium-capsule sensor, located just behind the capsule lever assembly.
3
Unscrew the 2 Phillips PH0 screws that hold the button panel to the front of the chassis.
4
Slide the button panel forward and lift it out together with the integrated LED indicators and the capsule sensor.
RESULT
• Button panel (35 g) • Capsule sensor (18 g)
CONTINUES AS
• Chassis (no panel) (1847 g)
TOOLS
JST connector tool, Phillips PH0 screwdriver, Hands
Bialetti Gioia
8 / 13

## Slide 9
ACTION GROUP 4
Extract pump, tubing and flow meter together
Atomic actions are grouped under their parent disassembly operation.
Source: Chassis (no panel) (1847 g)
explicit source
ATOMIC ACTIONS
1
Place a container under the chassis to catch ~30 mL of residual water that will drip from the tubing during removal.
2
Release the spring clamp on the silicone tube from the tank valve to the pump inlet; slide the tube off the barb.
3
Release the spring clamps on the silicone tubes from the pump outlet to the flow meter, and from the flow meter to the thermoblock inlet.
4
Unplug the 2-pin power connector that supplies the pump from the main PCB.
5
Unscrew the 2 Phillips PH1 screws holding the pump bracket to the chassis, then lift the pump together with the flow meter and the tubing as a single hydraulic assembly.
RESULT
• Vibration pump (185 g) • Silicone tubing (22 g) • Flow meter (28 g)
CONTINUES AS
• Chassis (no hydraulic) (1612 g)
TOOLS
Container, Hose clamp pliers, Hands, Phillips PH1 screwdriver
Bialetti Gioia
9 / 13

## Slide 10
ACTION GROUP 5
Extract main PCB, wiring harness and power cord
Atomic actions are grouped under their parent disassembly operation.
Source: Chassis (no hydraulic) (1612 g)
explicit source
ATOMIC ACTIONS
1
Unplug all remaining JST connectors from the main PCB: thermostat lead, thermoblock heater lead, pump triac lead.
2
Disconnect the mains input wires from the PCB screw terminals (LIVE / NEUTRAL / EARTH).
3
Cut any cable ties that fix the wiring harness to the chassis ribs.
4
Unscrew the 4 Phillips PH0 screws securing the PCB to its plastic tray and lift the board out.
5
Pull the wiring harness and the power cord through the chassis cut-out as a single bundle.
RESULT
• Main PCB (55 g) • Wiring harness (70 g) • Power cord (140 g)
CONTINUES AS
• Chassis (only thermoblock) (1347 g)
TOOLS
JST connector tool, Phillips PH0 screwdriver, Side cutters, Hands
Bialetti Gioia
10 / 13

## Slide 11
ACTION GROUP 6
Extract the thermoblock assembly and free the chassis frame
Atomic actions are grouped under their parent disassembly operation.
Source: Chassis (only thermoblock) (1347 g)
explicit source
ATOMIC ACTIONS
1
Verify the machine has been unplugged for at least 30 minutes so the thermoblock has fully cooled before touching the metal body.
2
Disconnect the two faston terminals of the heating element from the harness, and the 2-pin JST of the safety thermostat.
3
Unscrew the brass nut at the thermoblock outlet (towards the brew chamber) using a 10 mm wrench; keep a cloth nearby for residual drips.
4
Unscrew the 2 Phillips PH1 screws of the thermoblock bracket on the chassis side wall.
5
Lift the thermoblock assembly vertically out of its seat.
RESULT
• Chassis frame (967 g)
CONTINUES AS
• Thermoblock assembly (380 g)
TOOLS
Heat-resistant gloves (precaution), Hands, 10 mm wrench, Phillips PH1 screwdriver
Bialetti Gioia
11 / 13

## Slide 12
ACTION GROUP 7
Mechanically disassemble the thermoblock into its leaves
Atomic actions are grouped under their parent disassembly operation.
Source: Thermoblock assembly (380 g)
explicit source
ATOMIC ACTIONS
1
Clamp the aluminium body in a bench vice with soft jaws to avoid marking the surface; keep the heating-element side accessible.
2
Unscrew the safety thermostat from its threaded seat on the body; it comes out as a single threaded brass capsule.
3
Push out the heating element from its dedicated tunnel inside the aluminium body, gently tapping with a soft mallet if needed.
4
Separate the stainless-steel tube (water path) from the aluminium body; depending on the design, this may require a press or destructive cut.
RESULT
• Thermoblock fasteners (20 g) • Heating element (45 g) • Safety thermostat (15 g) • Aluminium body (240 g) • Stainless tube (60 g)
CONTINUES AS
End of this branch
TOOLS
Bench vice with soft jaws, Hex key (typically 4 mm), Soft mallet, Press / saw (destructive option)
Bialetti Gioia
12 / 13

## Slide 13
EXPORT COMPLETE
7 action groups prepared
The PowerPoint remains fully editable: text, tables, images and component information can be revised after export.
Bialetti Gioia
Bialetti Gioia
13 / 13