## Slide 1
FUTURDATA THESIS
Disassembly Guide
Air fryer Philips HD9252
PPTX export • 16 action group(s) • depth: DepthMode.FULL • schema 1.1
Nominal weight 4500 g
PRODUCT IMAGE
Air fryer Philips HD9252
1 / 23

## Slide 2
PROJECT OVERVIEW
Export scope and model summary
PRODUCT ID
2327511012176
ACTION GROUPS
16
BOM COMPONENTS
18
VALIDATION ISSUES
6
PRODUCT DATA
Name: Air fryer Philips HD9252 Weight: 4500 g Material: 6 Color: 4 Depth mode: DepthMode.FULL
EXPORT BEHAVIOUR
• Parent operation and atomic actions stay grouped. • Output components and remaining assembly are shown. • Text and images remain editable in PowerPoint. • Unknown branch sources are never guessed. • Source JSON is opened read-only and never modified.
Air fryer Philips HD9252
2 / 23

## Slide 3
VALIDATION
Model warnings and errors
Each issue is localized to the corresponding JSON element when possible.
SEVERITY.WARNING · mass_balance
Mass imbalance: leaf components sum to 3304 but the product weighs 4500 (26.6% off).
Location: node_ids=[2327511012176]
WARNING · step_mass_balance
Input 'Air fryer Philips HD9252' weighs 4500; outputs plus continuation weigh 3400 (24.4% difference).
Location: steps[0]
WARNING · step_mass_balance
Input 'Inferior body unscrewed' weighs 2612; outputs plus continuation weigh 2652 (1.5% difference).
Location: steps[5]
WARNING · step_mass_balance
Input 'Basket' weighs 400; outputs plus continuation weigh 250 (37.5% difference).
Location: steps[10]
WARNING · step_mass_balance
Input 'Tray with handle' weighs 250; outputs plus continuation weigh 254 (1.6% difference).
Location: steps[11]
WARNING · step_mass_balance
Input 'Handle without screws' weighs 142; outputs plus continuation weigh 152 (7.0% difference).
Location: steps[13]
Air fryer Philips HD9252
3 / 23

## Slide 4
PREPARATION
Tools and safety notices
Aggregated from step-level and atomic-action metadata.
TOOLS REQUIRED
• No tools are specified in this model.
SAFETY NOTICES
• No safety notices are specified in this model.
Air fryer Philips HD9252
4 / 23

## Slide 5
BILL OF MATERIALS
Recovered components — page 1 of 2
ID | Component | Weight | Material | Color | Quality | Destination
2327511009360 | Plastic cover (8 hooks) | 120 g | 1 | 4 | — | —
2327511018832 | 4 Angular screw (12.4 mm) | 8 g | 2 | 8 | — | —
2327511015248 | 2 Transformer screws (39.5 mm) | 10 g | 2 | 8 | — | —
2327511007568 | Transformer top piece | 40 g | 2 | 8 | — | —
2327528055824 | Cables (brown and white) | 20 g | 6 | 10 | — | —
2327511013008 | Transformer | 600 g | 2 | 8 | — | —
2327415634064 | Inferior body without transformer | 1992 g | 2 | 8 | — | —
2327511020560 | Rear panel board | 30 g | 1 | 4 | — | —
2327415619728 | Top without motherboard | 170 g | 1 | 4 | — | —
Air fryer Philips HD9252
5 / 23

## Slide 6
BILL OF MATERIALS
Recovered components — page 2 of 2
ID | Component | Weight | Material | Color | Quality | Destination
2327511014992 | Motherboard Touch Screen | 50 g | 8 | 2 | — | —
2327511061072 | 2 Top Screws (14.8 mm) | 4 g | 2 | 8 | — | —
2327511014800 | Tray | 100 g | 2 | 4 | — | —
2327511008464 | 4 Frontal Screws (14.8 mm) | 8 g | 2 | 8 | — | —
2327511009232 | Rear panel | 25 g | 1 | 4 | — | —
2327511016336 | Spring | 10 g | 1 | 8 | — | —
2327511011216 | Front of the latch | 10 g | 1 | 4 | — | —
2327511010640 | Latch Button | 10 g | 1 | 8 | — | —
2327528033168 | Handle without latch and button | 97 g | 1 | 4 | — | —
Air fryer Philips HD9252
6 / 23

## Slide 7
ACTION GROUP 1
remove the tray
Atomic actions are grouped under their parent disassembly operation.
Source: Air fryer Philips HD9252 (4500 g)
explicit source
ATOMIC ACTIONS
1
remove the tray
RESULT
• No separate output component encoded
CONTINUES AS
• Body HD9252 (3000 g) • Basket (400 g)
TOOLS
No tools specified
Air fryer Philips HD9252
7 / 23

## Slide 8
ACTION GROUP 2
remove the cover
Atomic actions are grouped under their parent disassembly operation.
Source: Body HD9252 (3000 g)
explicit source
ATOMIC ACTIONS
1
Insert a nylon spudger underneath
2
Leverage the tool and pop off each of the eight tabs
RESULT
• Plastic cover (8 hooks) (120 g)
CONTINUES AS
• Body without cover (2880 g)
TOOLS
No tools specified
Material: 1 · Color: 4
Air fryer Philips HD9252
8 / 23

## Slide 9
ACTION GROUP 3
unscrew(JIS #1)
Atomic actions are grouped under their parent disassembly operation.
Source: Body without cover (2880 g)
explicit source
ATOMIC ACTIONS
1
unscrew(JIS #1)
RESULT
• 4 Angular screw (12.4 mm) (8 g)
CONTINUES AS
• Body without cover (2872 g)
TOOLS
No tools specified
Material: 2 · Color: 8
Air fryer Philips HD9252
9 / 23

## Slide 10
ACTION GROUP 4
lift
Atomic actions are grouped under their parent disassembly operation.
Source: Body without cover (2872 g)
explicit source
ATOMIC ACTIONS
1
lift
RESULT
• No separate output component encoded
CONTINUES AS
• Inferior body (2622 g) • Top (250 g)
TOOLS
No tools specified
Air fryer Philips HD9252
10 / 23

## Slide 11
ACTION GROUP 5
unscrew
Atomic actions are grouped under their parent disassembly operation.
Source: Inferior body (2622 g)
explicit source
ATOMIC ACTIONS
1
unscrew
RESULT
• 2 Transformer screws (39.5 mm) (10 g)
CONTINUES AS
• Inferior body unscrewed (2612 g)
TOOLS
No tools specified
Material: 2 · Color: 8
Air fryer Philips HD9252
11 / 23

## Slide 12
ACTION GROUP 6
remove
Atomic actions are grouped under their parent disassembly operation.
Source: Inferior body unscrewed (2612 g)
explicit source
ATOMIC ACTIONS
1
remove
RESULT
• Transformer top piece (40 g)
CONTINUES AS
• Inferior body without top piece (2612 g)
TOOLS
No tools specified
Material: 2 · Color: 8
Air fryer Philips HD9252
12 / 23

## Slide 13
ACTION GROUP 7
remove cables
Atomic actions are grouped under their parent disassembly operation.
Source: Inferior body without top piece (2612 g)
explicit source
ATOMIC ACTIONS
1
Remove the brown and white wire attached
2
Disconnect
RESULT
• Cables (brown and white) (20 g)
CONTINUES AS
• Inferior body without cables (2592 g)
TOOLS
No tools specified
Material: 6 · Color: 10
Air fryer Philips HD9252
13 / 23

## Slide 14
ACTION GROUP 8
extract
Atomic actions are grouped under their parent disassembly operation.
Source: Inferior body without cables (2592 g)
explicit source
ATOMIC ACTIONS
1
extract
RESULT
• Transformer (600 g) • Inferior body without transformer (1992 g)
CONTINUES AS
End of this branch
TOOLS
No tools specified
Material: 2 · Color: 8
Air fryer Philips HD9252
14 / 23

## Slide 15
ACTION GROUP 9
remove the panel
Atomic actions are grouped under their parent disassembly operation.
Source: Top (250 g)
explicit source
ATOMIC ACTIONS
1
Insert a nylon spudger underneath the top
2
Leverage the tool and pop off
RESULT
• Rear panel board (30 g)
CONTINUES AS
• Top without panel (220 g)
TOOLS
No tools specified
Material: 1 · Color: 4
Air fryer Philips HD9252
15 / 23

## Slide 16
ACTION GROUP 10
remove the motherboard
Atomic actions are grouped under their parent disassembly operation.
Source: Top without panel (220 g)
explicit source
ATOMIC ACTIONS
1
remove the motherboard
RESULT
• Top without motherboard (170 g) • Motherboard Touch Screen (50 g)
CONTINUES AS
End of this branch
TOOLS
No tools specified
Material: 1 · Color: 4
Air fryer Philips HD9252
16 / 23

## Slide 17
ACTION GROUP 11
pull
Atomic actions are grouped under their parent disassembly operation.
Source: Basket (400 g)
explicit source
ATOMIC ACTIONS
1
pull
RESULT
• No separate output component encoded
CONTINUES AS
• Tray with handle (250 g)
TOOLS
No tools specified
Air fryer Philips HD9252
17 / 23

## Slide 18
ACTION GROUP 12
unscrew 4 scres
Atomic actions are grouped under their parent disassembly operation.
Source: Tray with handle (250 g)
explicit source
ATOMIC ACTIONS
1
unscrew 4 scres
RESULT
• 2 Top Screws (14.8 mm) (4 g) • Tray (100 g)
CONTINUES AS
• Handle (150 g)
TOOLS
No tools specified
Material: 2 · Color: 8
Air fryer Philips HD9252
18 / 23

## Slide 19
ACTION GROUP 13
unscrew
Atomic actions are grouped under their parent disassembly operation.
Source: Handle (150 g)
explicit source
ATOMIC ACTIONS
1
unscrew
RESULT
• 4 Frontal Screws (14.8 mm) (8 g)
CONTINUES AS
• Handle without screws (142 g)
TOOLS
No tools specified
Material: 2 · Color: 8
Air fryer Philips HD9252
19 / 23

## Slide 20
ACTION GROUP 14
pry out
Atomic actions are grouped under their parent disassembly operation.
Source: Handle without screws (142 g)
explicit source
ATOMIC ACTIONS
1
pry out
RESULT
• Rear panel (25 g)
CONTINUES AS
• Handle without panel (127 g)
TOOLS
No tools specified
Material: 1 · Color: 4
Air fryer Philips HD9252
20 / 23

## Slide 21
ACTION GROUP 15
remove the pring
Atomic actions are grouped under their parent disassembly operation.
Source: Handle without panel (127 g)
explicit source
ATOMIC ACTIONS
1
push the spring down
2
slide the spring out
RESULT
• Spring (10 g)
CONTINUES AS
• Handle without spring (117 g)
TOOLS
No tools specified
Material: 1 · Color: 8
Air fryer Philips HD9252
21 / 23

## Slide 22
ACTION GROUP 16
remove
Atomic actions are grouped under their parent disassembly operation.
Source: Handle without spring (117 g)
explicit source
ATOMIC ACTIONS
1
remove
RESULT
• Front of the latch (10 g) • Latch Button (10 g) • Handle without latch and button (97 g)
CONTINUES AS
End of this branch
TOOLS
No tools specified
Material: 1 · Color: 4
Air fryer Philips HD9252
22 / 23

## Slide 23
EXPORT COMPLETE
16 action groups prepared
The PowerPoint remains fully editable: text, tables, images and component information can be revised after export.
Air fryer Philips HD9252
Air fryer Philips HD9252
23 / 23