## Slide 1
FUTURDATA THESIS
Disassembly Guide
Washing machine
PPTX export • 18 action group(s) • depth: DepthMode.FULL • schema 1.1
Nominal weight Unknown
PRODUCT IMAGE
Washing machine
1 / 30

## Slide 2
PROJECT OVERVIEW
Export scope and model summary
PRODUCT ID
2632634200720
ACTION GROUPS
18
BOM COMPONENTS
35
VALIDATION ISSUES
20
PRODUCT DATA
Name: Washing machine Weight: Unknown Material: Unknown Color: Unknown Depth mode: DepthMode.FULL
EXPORT BEHAVIOUR
• Parent operation and atomic actions stay grouped. • Output components and remaining assembly are shown. • Text and images remain editable in PowerPoint. • Unknown branch sources are never guessed. • Source JSON is opened read-only and never modified.
Washing machine
2 / 30

## Slide 3
VALIDATION
Model warnings and errors — 1
Each issue is localized to the corresponding JSON element when possible.
SEVERITY.INFO · mass_balance
Mass balance not verifiable: the product has no weight; 35 component(s) have no weight.
Location: node_ids=[2632506255568, 2632543935952, 2632634200912, 2632634201168, 2632634201616, 2632634201872, 2632634202256, 2632634202448, 2632634202704, 2632634202960, 2632634203344, 2632634203600, 2632634237200, 2632634237264, 2632634237648, 2632634237904, 2632634238224, 2632634238480, 2632634238608, 2632634238864, 2632634239184, 2632634239568, 2632634239760, 2632634240208, 2632634240336, 2632634240592, 2632634240976, 2632634241168, 2632634241616, 2632634241680, 2632634242064, 2632634242448, 2632634243088, 2632634243344, 2632634243536]
WARNING · images
Image file not found: images/manual_page_24.png
Location: steps[0].actions[0].image
WARNING · images
Image file not found: images/manual_page_24.png
Location: steps[1].actions[0].image
WARNING · images
Image file not found: images/manual_page_24.png
Location: steps[2].actions[0].image
WARNING · images
Image file not found: images/manual_page_25.png
Location: steps[3].actions[0].image
WARNING · images
Image file not found: images/manual_page_26.png
Location: steps[4].actions[0].image
Washing machine
3 / 30

## Slide 4
VALIDATION
Model warnings and errors — 2
Each issue is localized to the corresponding JSON element when possible.
WARNING · images
Image file not found: images/manual_page_28.png
Location: steps[5].actions[0].image
WARNING · images
Image file not found: images/manual_page_26.png
Location: steps[6].actions[0].image
WARNING · images
Image file not found: images/manual_page_26.png
Location: steps[7].actions[0].image
WARNING · images
Image file not found: images/manual_page_30.png
Location: steps[8].actions[0].image
WARNING · images
Image file not found: images/manual_page_27.png
Location: steps[9].actions[0].image
WARNING · images
Image file not found: images/manual_page_27.png
Location: steps[10].actions[0].image
Washing machine
4 / 30

## Slide 5
VALIDATION
Model warnings and errors — 3
Each issue is localized to the corresponding JSON element when possible.
WARNING · images
Image file not found: images/manual_page_28.png
Location: steps[11].actions[0].image
WARNING · images
Image file not found: images/manual_page_28.png
Location: steps[12].actions[0].image
WARNING · images
Image file not found: images/manual_page_28.png
Location: steps[13].actions[0].image
WARNING · images
Image file not found: images/manual_page_28.png
Location: steps[14].actions[0].image
WARNING · images
Image file not found: images/manual_page_29.png
Location: steps[15].actions[0].image
WARNING · images
Image file not found: images/manual_page_29.png
Location: steps[16].actions[0].image
Washing machine
5 / 30

## Slide 6
VALIDATION
Model warnings and errors — 4
Each issue is localized to the corresponding JSON element when possible.
WARNING · images
Image file not found: images/manual_page_30.png
Location: steps[16].actions[2].image
WARNING · images
Image file not found: images/manual_page_29.png
Location: steps[17].actions[0].image
Washing machine
6 / 30

## Slide 7
PREPARATION
Tools and safety notices
Aggregated from step-level and atomic-action metadata.
TOOLS REQUIRED
• Coin • Long bar (conditional foreign-material retrieval)
SAFETY NOTICES
• No safety notices are specified in this model.
Washing machine
7 / 30

## Slide 8
BILL OF MATERIALS
Recovered components — page 1 of 4
ID | Component | Weight | Material | Color | Quality | Destination
2632634201168 | Top plate | Unknown | Unknown | Unknown | — | —
2632634200912 | Top-plate screws (2) | Unknown | Unknown | Unknown | — | —
2632634201616 | Detergent drawer | Unknown | Unknown | Unknown | — | —
2632634201872 | Control-panel screws (2) | Unknown | Unknown | Unknown | — | —
2632543935952 | Control-panel PWB assembly | Unknown | Unknown | Unknown | — | —
2632634202256 | Control-panel housing | Unknown | Unknown | Unknown | — | —
2632634202448 | PWB securing screws (5) | Unknown | Unknown | Unknown | — | —
2632634202704 | Dispenser assembly with associated hoses / bellows | Unknown | Unknown | Unknown | — | —
2632634202960 | Dispenser screws (2) | Unknown | Unknown | Unknown | — | —
Washing machine
8 / 30

## Slide 9
BILL OF MATERIALS
Recovered components — page 2 of 4
ID | Component | Weight | Material | Color | Quality | Destination
2632634203344 | Inlet-valve assembly | Unknown | Unknown | Unknown | — | —
2632634203600 | Inlet-valve screws (2) | Unknown | Unknown | Unknown | — | —
2632634237264 | Lower cover | Unknown | Unknown | Unknown | — | —
2632634237200 | Lower-cover screw (1) | Unknown | Unknown | Unknown | — | —
2632634237904 | Door assembly with hinge / bracket | Unknown | Unknown | Unknown | — | —
2632634237648 | Door hinge screws (2) | Unknown | Unknown | Unknown | — | —
2632634238480 | Cabinet-side gasket clamp | Unknown | Unknown | Unknown | — | —
2632634238224 | Door-lock switch assembly | Unknown | Unknown | Unknown | — | —
2632634238608 | Door-lock screws (2) | Unknown | Unknown | Unknown | — | —
Washing machine
9 / 30

## Slide 10
BILL OF MATERIALS
Recovered components — page 3 of 4
ID | Component | Weight | Material | Color | Quality | Destination
2632634239184 | Cabinet cover | Unknown | Unknown | Unknown | — | —
2632634238864 | Cabinet-cover screws (count unspecified) | Unknown | Unknown | Unknown | — | —
2632634239760 | Tub-side gasket clamp | Unknown | Unknown | Unknown | — | —
2632634239568 | Gasket assembly | Unknown | Unknown | Unknown | — | —
2632634240208 | Back cover with retained hardware | Unknown | Unknown | Unknown | — | —
2632506255568 | Drive belt | Unknown | Unknown | Unknown | — | —
2632634240336 | Pulley bolt | Unknown | Unknown | Unknown | — | —
2632634240592 | Drive pulley | Unknown | Unknown | Unknown | — | —
2632634240976 | Motor assembly | Unknown | Unknown | Unknown | — | —
Washing machine
10 / 30

## Slide 11
BILL OF MATERIALS
Recovered components — page 4 of 4
ID | Component | Weight | Material | Color | Quality | Destination
2632634241168 | Motor-bracket screws (2) | Unknown | Unknown | Unknown | — | —
2632634241680 | Damper assembly (illustrated) | Unknown | Unknown | Unknown | — | —
2632634241616 | Removed damper hinge/pin - do not reuse | Unknown | Unknown | Unknown | — | —
2632634242448 | Drain pump | Unknown | Unknown | Unknown | — | —
2632634242064 | Drain-pump screws (2) | Unknown | Unknown | Unknown | — | —
2632634243088 | Heater assembly with retained M6 nut | Unknown | Unknown | Unknown | — | —
2632634243536 | Thermistor assembly | Unknown | Unknown | Unknown | — | —
2632634243344 | Remaining chassis, tub, drum and unmodelled parts | Unknown | Unknown | Unknown | — | —
Washing machine
11 / 30

## Slide 12
ACTION GROUP 1
Remove top plate
Atomic actions are grouped under their parent disassembly operation.
Source: Washing machine (Unknown)
explicit source
ATOMIC ACTIONS
1
Unplug the machine from the electrical outlet before disassembly or repair (manual warning).
2
Remove the two screws at the back of the top plate.
3
Slide the top plate backward, then lift it upward as illustrated.
Action 1
RESULT
• Top plate (Unknown) • Top-plate screws (2) (Unknown)
CONTINUES AS
• Machine without top plate (Unknown)
Washing machine
12 / 30

## Slide 13
ACTION GROUP 2
Remove control panel
Atomic actions are grouped under their parent disassembly operation.
Source: Machine without top plate (Unknown)
explicit source
ATOMIC ACTIONS
1
Disconnect the PWB assembly connector from the main lead-wire assembly.
2
Pull out the detergent drawer and remove the two screws shown.
3
Press the upper hooks down and pull the control panel away.
Action 1
RESULT
• Detergent drawer (Unknown) • Control-panel screws (2) (Unknown)
CONTINUES AS
• Control panel with PWB (Unknown) • Machine without control panel (Unknown)
Washing machine
13 / 30

## Slide 14
ACTION GROUP 3
Separate PWB from panel
Atomic actions are grouped under their parent disassembly operation.
Source: Control panel with PWB (Unknown)
explicit source
ATOMIC ACTIONS
1
Remove the five screws securing the PWB assembly to the removed control panel.
2
Separate the PWB assembly from the control panel.
Action 1
RESULT
• Control-panel PWB assembly (Unknown) • Control-panel housing (Unknown) • PWB securing screws (5) (Unknown)
CONTINUES AS
End of this branch
Washing machine
14 / 30

## Slide 15
ACTION GROUP 4
Remove dispenser
Atomic actions are grouped under their parent disassembly operation.
Source: Machine without control panel (Unknown)
explicit source
ATOMIC ACTIONS
1
Prerequisites already completed: top plate and detergent drawer removed.
2
Remove the two dispenser screws shown on this page.
3
Detach the hose and its clamps as illustrated.
4
Detach the ventilation bellows and the water-inlet bellows at the tub, and remove the dispenser assembly. Follow the illustrated option fitted to the machine.
Action 1
RESULT
• Dispenser assembly with associated hoses / bellows (Unknown) • Dispenser screws (2) (Unknown)
CONTINUES AS
• Machine without dispenser (Unknown)
Washing machine
15 / 30

## Slide 16
ACTION GROUP 5
Remove inlet valve
Atomic actions are grouped under their parent disassembly operation.
Source: Machine without dispenser (Unknown)
explicit source
ATOMIC ACTIONS
1
Disconnect the inlet-valve wiring receptacle.
2
Remove the two screws at the back and detach the inlet valve.
3
Reconnection reference from the manual: valve 1 (MAIN): White/Black-Black; valve 2 (PRE): Black-Gray; valve 3 (HOT): Blue/White-Black. Apply only to the illustrated configuration.
Action 1
RESULT
• Inlet-valve assembly (Unknown) • Inlet-valve screws (2) (Unknown)
CONTINUES AS
• Machine without inlet valve (Unknown)
Washing machine
16 / 30

## Slide 17
ACTION GROUP 6
Drain and clean pump filter
Atomic actions are grouped under their parent disassembly operation.
Source: Machine without inlet valve (Unknown)
explicit source
ATOMIC ACTIONS
1
Maintenance procedure: open the lower cover cap with a coin and pull out the drain hose using the drain plug as illustrated.
2
Place a vessel to collect the water, then remove the drain plug and let the remaining water drain.
3
When the flow stops, turn the pump filter counterclockwise and remove foreign material.
4
Refit the filter clockwise, restore the drain plug, and close the lower cover cap as instructed.
Action 1
RESULT
• No separate output component encoded
CONTINUES AS
• Machine after filter servicing (Unknown)
Washing machine
17 / 30

## Slide 18
ACTION GROUP 7
Remove lower cover
Atomic actions are grouped under their parent disassembly operation.
Source: Machine after filter servicing (Unknown)
explicit source
ATOMIC ACTIONS
1
Open the lower cover cap with a coin.
2
Remove the retaining screw and pull the lower cover in the illustrated arrow direction.
Action 1
RESULT
• Lower cover (Unknown) • Lower-cover screw (1) (Unknown)
CONTINUES AS
• Machine without lower cover (Unknown)
Washing machine
18 / 30

## Slide 19
ACTION GROUP 8
Remove door
Atomic actions are grouped under their parent disassembly operation.
Source: Machine without lower cover (Unknown)
explicit source
ATOMIC ACTIONS
1
Open the door fully.
2
Hold the bracket inside the cabinet cover while removing the two hinge screws.
3
Remove the door assembly while retaining control of the inner bracket.
Action 1
RESULT
• Door assembly with hinge / bracket (Unknown) • Door hinge screws (2) (Unknown)
CONTINUES AS
• Machine without door (Unknown)
Washing machine
19 / 30

## Slide 20
ACTION GROUP 9
Remove door-lock switch
Atomic actions are grouped under their parent disassembly operation.
Source: Machine without door (Unknown)
explicit source
ATOMIC ACTIONS
1
Remove the cabinet-side gasket clamp and release the gasket from the cabinet opening.
2
Remove the two screws securing the door lock.
3
Disconnect the door-lock wiring connector and remove the switch assembly.
Action 1
RESULT
• Cabinet-side gasket clamp (Unknown) • Door-lock switch assembly (Unknown) • Door-lock screws (2) (Unknown)
CONTINUES AS
• Machine without door-lock switch (Unknown)
Washing machine
20 / 30

## Slide 21
ACTION GROUP 10
Remove cabinet cover
Atomic actions are grouped under their parent disassembly operation.
Source: Machine without door-lock switch (Unknown)
explicit source
ATOMIC ACTIONS
1
Prerequisites already completed: control panel, lower cover, and cabinet-side gasket clamp removed; gasket released from the cabinet opening.
2
Remove the two cabinet-cover screws indicated in the first illustration.
3
Remove the remaining upper and lower cabinet-cover screws shown and detach the cabinet cover. The excerpt does not establish a total screw count.
Action 1
RESULT
• Cabinet cover (Unknown) • Cabinet-cover screws (count unspecified) (Unknown)
CONTINUES AS
• Machine without cabinet cover (Unknown)
Washing machine
21 / 30

## Slide 22
ACTION GROUP 11
Remove gasket
Atomic actions are grouped under their parent disassembly operation.
Source: Machine without cabinet cover (Unknown)
explicit source
ATOMIC ACTIONS
1
Release the tub-side gasket clamp and remove the gasket assembly.
2
Reassembly note: position the gasket drain hole at the bottom and use the arrow on the tub cover as a reference.
Action 1
RESULT
• Tub-side gasket clamp (Unknown) • Gasket assembly (Unknown)
CONTINUES AS
• Machine without gasket (Unknown)
Washing machine
22 / 30

## Slide 23
ACTION GROUP 12
Remove back cover
Atomic actions are grouped under their parent disassembly operation.
Source: Machine without gasket (Unknown)
explicit source
ATOMIC ACTIONS
1
Remove the back cover to access the pulley and motor. This excerpt does not specify the cover fastener count or a detailed release procedure.
Action 1
RESULT
• Back cover with retained hardware (Unknown)
CONTINUES AS
• Machine without back cover (Unknown)
Washing machine
23 / 30

## Slide 24
ACTION GROUP 13
Remove belt and pulley
Atomic actions are grouped under their parent disassembly operation.
Source: Machine without back cover (Unknown)
explicit source
ATOMIC ACTIONS
1
Turn the pulley while taking off the drive belt, as illustrated.
2
Remove the pulley bolt and pull off the pulley.
Action 1
RESULT
• Drive belt (Unknown) • Pulley bolt (Unknown) • Drive pulley (Unknown)
CONTINUES AS
• Machine without belt and pulley (Unknown)
Washing machine
24 / 30

## Slide 25
ACTION GROUP 14
Remove motor
Atomic actions are grouped under their parent disassembly operation.
Source: Machine without belt and pulley (Unknown)
explicit source
ATOMIC ACTIONS
1
Remove the two screws from the motor bracket.
2
Push the motor in the illustrated arrow direction to remove it.
3
Reassembly note: ensure the motor mounting bushings remain fitted to the bracket.
Action 1
RESULT
• Motor assembly (Unknown) • Motor-bracket screws (2) (Unknown)
CONTINUES AS
• Machine without motor (Unknown)
Washing machine
25 / 30

## Slide 26
ACTION GROUP 15
Remove damper
Atomic actions are grouped under their parent disassembly operation.
Source: Machine without motor (Unknown)
explicit source
ATOMIC ACTIONS
1
Press the retaining snap and pull out the damper hinge/pin shown in the illustration to release the damper.
2
Do not reuse the removed hinge/pin: the manual warns that it may come loose during operation.
Action 1
RESULT
• Damper assembly (illustrated) (Unknown) • Removed damper hinge/pin - do not reuse (Unknown)
CONTINUES AS
• Machine without illustrated damper (Unknown)
Washing machine
26 / 30

## Slide 27
ACTION GROUP 16
Remove drain pump
Atomic actions are grouped under their parent disassembly operation.
Source: Machine without illustrated damper (Unknown)
explicit source
ATOMIC ACTIONS
1
Detach the pump outlet hose.
2
Detach the tub-to-pump bellows.
3
Remove the cap identified in the manual as Remaining Hose.
4
Disconnect the pump wiring.
5
Remove the two securing screws, then remove the pump.
Action 1
RESULT
• Drain pump (Unknown) • Drain-pump screws (2) (Unknown)
CONTINUES AS
• Machine without drain pump (Unknown)
Washing machine
27 / 30

## Slide 28
ACTION GROUP 17
Remove heater
Atomic actions are grouped under their parent disassembly operation.
Source: Machine without drain pump (Unknown)
explicit source
ATOMIC ACTIONS
1
Loosen the M6 heater nut and pull out the heater.
2
Reassembly note: insert the heater into the heater clip at the bottom of the tub.
3
Optional service task, printed page 30: if foreign material is trapped between the drum and tub, remove it through the heater opening using a long bar after the heater has been removed.
Action 1
Action 3
RESULT
• Heater assembly with retained M6 nut (Unknown)
CONTINUES AS
• Machine without heater (Unknown)
Washing machine
28 / 30

## Slide 29
ACTION GROUP 18
Remove thermistor
Atomic actions are grouped under their parent disassembly operation.
Source: Machine without heater (Unknown)
explicit source
ATOMIC ACTIONS
1
Pull out the thermistor by holding its bracket. Do not pull its wire; the manual warns that this can break it.
2
Reassembly note: make sure the thermistor fits tightly back into its bushing.
Action 1
RESULT
• Thermistor assembly (Unknown) • Remaining chassis, tub, drum and unmodelled parts (Unknown)
CONTINUES AS
End of this branch
Washing machine
29 / 30

## Slide 30
EXPORT COMPLETE
18 action groups prepared
The PowerPoint remains fully editable: text, tables, images and component information can be revised after export.
Washing machine
Washing machine
30 / 30